## Slide 1: Voltage Glitching Intel Microcode
Federico Cerutti / ceres-c
Università degli Studi di Brescia
Previously: VU Amsterdam

## Slide 2: TL;DR
What: Glitch Intel microcode
How: Voltage glitching
Why: Attack microcode update
Did it work? Kinda no?

## Slide 3: CPU 101
Custom Processing Unit: Tracing and Patching Intel Atom Microcode – Pietro Borrello, Martin Schwarzl
Notes: Microcoded CPU! For performance

## Slide 4: Arch → μArch instructions
Fetch
Decode queue
  (Instruction fusion)
Decode:
Allocation queue
…
We pretend speculative execution does not exist
Simple decoder
Complex decoder
‌Microcode sequencer
1 x86 = 1 μ-op
1 x86 = 3/4 μ-op
1 x86 = n μ-op

## Slide 5: Microcode Sequencer
Implements complex instructions
Does not execute code directly, however has:
  ROM
  RAM
  Registers
    Instruction pointer
  Peripherals
Updatable
  Signed updates

## Slide 6: Previously on: Red Unlock
Intel products have extensive testing & debugging features
Can be activated via:
  Hardware straps (preproduction only)
  Efuses (disabled on non-dev)
  JTAG password
  Software

## Slide 7: Previously on: Red Unlock
Intel products have extensive testing & debugging features
Can be activated via:
  Hardware straps (preproduction only)
  Efuses (disabled on non-dev)
  JTAG password
  Software
Introducing: Intel ME exploits on Goldmont SoCs
Ermolov, Goryachy and Sklyarov
Notes: Ermolov, Goryachy and Sklyarov

## Slide 8: Previously on: Red Unlock - Goldmont
Exploit ME 11
Extract microcode with JTAG
Reverse engineer architecture
Find architectural instructions to read/write microarchitectural state
???
Write your own microcode!
Ermolov, Goryachy and Sklyarov
1: https://github.com/pietroborrello/CustomProcessingUnit/
2: https://github.com/zanderdk/lib-micro/
CustomProcessingUnit1
lib-micro2

## Slide 9: Custom Microcode
XLAT
rdrand
cpuid
vmenter
…
MSROM |  |  | 

## Slide 10: Custom Microcode
XLAT
rdrand
cpuid
vmenter
…
MSROM |  |  | 
match&patch | 
MSRAM |  |  | 

## Slide 11: Previously on: x86 Voltage Glitching
Intel and AMD CPUs proven vulnerable to voltage fault injection
No changes to the power supply, leverage the PMIC1
Two ways:
  Software based: Plundervolt, VoltJockey
  Hardware based: VoltPillager, PMFault
Glitch x86 or secure enclaves
1: Power Management Integrated Chip

## Slide 12: Previously on: x86 Voltage Glitching
Intel and AMD CPUs proven vulnerable to voltage fault injection
No changes to the power supply, leverage the PMIC1
Two ways:
  Software based: Plundervolt, VoltJockey
  Hardware based: VoltPillager, PMFault
Glitch x86 or secure enclaves
1: Power Management Integrated Chip
How about microcode?

## Slide 13: Roadmap
Find hardware
  Must be red unlocked
  Possibly simple I/O
Build software setup
  x86 convoluted bootstrap
  Make it fast
  How2microcode?
Port Plundervolt x86 results
Attack custom microprograms
Attack microcode update

## Slide 14: Pick (red unlocked) hardware
Up Squared 2
Intel Pentium N4200
coreboot
GPIO
lib-micro
Gigabyte BRIX BPCE-3350C 1
Intel Celeron N3350
AMI BIOS
Ermolov et al.
1: https://github.com/ptresearch/IntelTXE-PoC
2: https://github.com/zanderdk/lib-micro/

## Slide 15: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | 

## Slide 16: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot

## Slide 17: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot
coreboot (32-bit) vs. microcode libs (64-bit) | 

## Slide 18: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot
coreboot (32-bit) vs. microcode libs (64-bit) | Port lib-micro

## Slide 19: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot
coreboot (32-bit) vs. microcode libs (64-bit) | Port lib-micro
Custom microcode in early boot halts CPU | 

## Slide 20: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot
coreboot (32-bit) vs. microcode libs (64-bit) | Port lib-micro
Custom microcode in early boot halts CPU | Find stable execution point
Up Squared + coreboot is the way to go
bootblock
romstage
postCAR
ramstage
payload
Cache-As-Ram
DRAM
Memory
location
coreboot
stage
target
~700 ms

## Slide 21: Software
Issue | Solution
BIOS boot time w/ red unlock > 2min | Target code in coreboot
coreboot (32-bit) vs. microcode libs (64-bit) | Port lib-micro
Custom microcode in early boot halts CPU | Find stable execution point
Up Squared + coreboot is the way to go
bootblock
romstage
postCAR
ramstage
payload
Cache-As-Ram
DRAM
Memory
location
coreboot
stage
target
~700 ms
(manually 🤡)

## Slide 22: Inject the glitch
Control the PMIC:
  Software
  Hardware
Bonus: find VCore
Thanks to Carlo Maragno

## Slide 23: Inject the glitch
Control the PMIC:
  ​Software
  Hardware
Bonus: find VCore
Thanks to Carlo Maragno

## Slide 24: Interjection: Glitch characteristics
1: Inspired by VoltPillager

## Slide 25: Interjection: Glitch characteristics
1: Inspired by VoltPillager

## Slide 26: Interjection: Glitch characteristics
A two-stage glitch1
1: Inspired by VoltPillager

## Slide 27: Slow PMIC - Workaround
A two-stage glitch1
1: Inspired by VoltPillager

## Slide 28: Injecting the glitch
Raspberry Pi Pico FTW
GPIO @ 3v3 :(
Modify Pi Pico
  IOVDD @ 1v8
  USB_VDD @ 3v3
  Swap SPI flash

## Slide 29: Getting them to talk
GPIO? Not really
  CPLD proxy
UART will do!
PMBus
UART
Glitcher
Up Squared

## Slide 30: Setup overview
5 components:
Target: Up Squared board
Glitcher: Raspberry Pi Pico
Host PC
Power supply
Oscilloscope
VCore probe
PMBus probe
Laboratory PSU
Oscilloscope
PMBus
UART
Glitcher
Up Squared
Host
5V
USB
USB

## Slide 31: Setup overview
5 components:
Target: Up Squared board
Glitcher: Raspberry Pi Pico
Host PC
Power supply
Oscilloscope
VCore probe
PMBus probe
Laboratory PSU
Oscilloscope
PMBus
UART
Glitcher
Up Squared
Host
5V
USB
USB

## Slide 32: Previous research: Plundervolt
Simple arithmetic operations can’t be glitched
  ADD/SUB, OR/XOR/AND: nope
IMUL can be faulted with:
  specific operands
  specific operand order, e.g.
    0x80000 * 0x4: Faulty
    0x4 * 0x80000: Not faulty
    0x80001 * 0x4: Not faulty

## Slide 33: x86 assembly: IMUL
Prepare operands
Multiply (twice)
Compare
Set dl[7:0] if different
Add dl[7:0] to cl[7:0]
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
AT&T syntax because coreboot
Normal: ecx = 0 Fault: ecx > 0

## Slide 34: x86 assembly: IMUL
IMUL can be glitched!
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
✔️

## Slide 35: x86 assembly: IMUL
IMUL can be glitched:
Regardless of operand order
  0x80000 * 0x4: Faulty
  0x4 * 0x80000: Faulty
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
❔

## Slide 36: x86 assembly: IMUL
IMUL can be glitched:
Regardless of operand order
  0x80000 * 0x4: Faulty
  0x4 * 0x80000: Faulty
  Is it CMP?
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
❔

## Slide 37: x86 assembly: IMUL
IMUL can be glitched:
Regardless of operand order
  0x80000 * 0x4: Faulty
  0x4 * 0x80000: Faulty
  Is it CMP?
Sometimes
  ecx = 0x200000
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
❔

## Slide 38: x86 assembly: IMUL
IMUL can be glitched:
Regardless of operand order
  0x80000 * 0x4: Faulty
  0x4 * 0x80000: Faulty
  Is it CMP?
Sometimes
  ecx = 0x200000 (0x4*0x80000)
  Is ADDB adding 32 bits?
  Register file issues?
movl $0x80000, %eax;
movl $0x4, %ebx;
movl %eax, %edx;
imull %ebx, %edx; # edx = 0x4*0x80000
movl %eax, %edi;
imull %ebx, %edi; # edi = 0x4*0x80000
cmp %edx, %edi;
setne %dl;
addb %dl, %cl;
❔

## Slide 39: x86 assembly: CMP
movl $0xAAAAAAAA, %eax;
movl $0xAAAAAAAA, %ebx;
cmp %eax, %ebx;
setne %dl;
addb %dl, %cl;
Prepare operands
Compare
Set dl[7:0] if different
Add dl[7:0] to cl[7:0]
Normal: ecx = 0 Fault: ecx > 0

## Slide 40: x86 assembly: CMP
movl $0xAAAAAAAA, %eax;
movl $0xAAAAAAAA, %ebx;
cmp %eax, %ebx;
setne %dl;
addb %dl, %cl;
Fault count
Occurences
Yup, CMP can be glitched 75% of the times
✔️

## Slide 41: x86 assembly: Register file
mov $0x0101, %eax;
movb %al, %bl;
add %ebx, %ecx;
Prepare operand
Move al[7:0] to bl[7:0]
Add ebx[31:0] to ecx[31:0]
Normal: ecx = i Fault: ecx > i
(i iterations)
Notes: Test:
Operations on sub-registers
Register rename

## Slide 42: x86 assembly: Register file
mov $0x0101, %eax;
movb %al, %bl;
add %ebx, %ecx;
Occurences
Probably not register file, but instructions skip
Return value
❔

## Slide 43: Custom microcode: ADDs
{
ADD_DSZ64_DRI(RCX, RCX, 1),
ADD_DSZ64_DRI(RCX, RCX, 1),
ADD_DSZ64_DRI(RCX, RCX, 1),
NOP_SEQWORD
}, /* ... */ {
ADD_DSZ64_DRI(RCX, RCX, 1),
NOP,
NOP,
END_SEQWORD
},
Add 1 to ecx, 10 times in a row
Replace RDRAND
Arch fault: ecx % 10 = 0
μarch fault: ecx % 10 ≠ 0
Normal: ecx = i*10
(i iterations)

## Slide 44: Custom microcode: ADDs
{
ADD_DSZ64_DRI(RCX, RCX, 1),
ADD_DSZ64_DRI(RCX, RCX, 1),
ADD_DSZ64_DRI(RCX, RCX, 1),
NOP_SEQWORD
}, /* ... */ {
ADD_DSZ64_DRI(RCX, RCX, 1),
NOP,
NOP,
END_SEQWORD
},
Replace RDRAND
Occurences
Both x86 and microcode instruction skip
Return value
✔️

## Slide 45: Previously on: Microcode updates
Documented in previous research
  Treat it as a gray box
  I hope it works like this
Secure (enough) cryptographic primitives

## Slide 46: Previously on: Microcode updates
Documented in previous research
  Treat it as a gray box
  I hope it works like this
Secure (enough) cryptographic primitives
Can we attack these?

## Slide 47: Microcode update: RSA modulus
Update is not constant-time
Texec vs Tref
Change signature
Apply update (fail)
Measure Tref (fail)
Glitch
Fault: Texec > Tref
Normal: Texec = Tref

## Slide 48: Microcode update: RSA modulus
Interesting timings :) Fail update :(
Occurences
Texec (cycles)
❔

## Slide 49: Microcode update: Signature
Update is not constant-time
Texec vs Tref
Change update content
Apply update (fail)
Measure Tref (fail)
Glitch
Fault: Texec > Tref
Normal: Texec = Tref

## Slide 50: Microcode update: Signature
Occurences
Texec (cycles)
Meh timings :( Fail update :(
❌

## Slide 51: Recap
Evidence of:
x86 arithmetic faults
x86 instruction skip
Register file weirdness
μ-instruction skip
Changed update program behavior
Future work:
Reverse engineer microcode update
  Why glitch not enough?
Replace PMIC
TOCTOU RSA modulus?
Unsigned microcode update rejected

## Slide 52: Questions, remarks, vituperation?
federico@ceres-c.it
https://ceres-c.it/
https://github.com/ceres-c/VU-Thesis

## Slide 53: Backup slides

## Slide 54: How to estimate voltages
Voltage (VID)
Time (μs)

## Slide 55: Signature check glitch fail
Time (μs)
Voltage (VID)
Voltage (VID)
Time (μs)
Notes: Left: x86 code
Right: ucode (it never dies, there is no low voltage)

## Slide 56: Signature check glitch fail
Voltage (VID)
Time (μs)
Notes: Left: ucode glitches in
Right: example image where we can see the voltage does not rise fast enough
The voltages where we have successes in glitching the ucoda update are low. Too low to be reached near the end of the update

## Slide 57: Why Goldmont only
"How We Achieved to Execute Arbitrary Ucode"

## Slide 58: Why microcode update is a lost cause
We don’t have the RC4 key
RC4 vulnerable to bit flips
But each uinstr/seqword has a CRC
From lib-micro docs